## Slide 1: Network Slicing in 5G Networks

## Slide 2
SL no. | USN . | Name | Email Id
1. | 1RV22CY039 | MEHAR KULKARNI | meharkulkarni.cy22@rvce.edu.in
2. | 1RV22CY057 | TANISHA AGARWAL | tanishaagarwal.cy22@rvce.edu.in
TEAM INTRODUCTION

## Slide 3
Introduction
Approach and Methodology
References
CONTENTS

## Slide 4: INTRODUCTION
What is Network Slicing?
Network slicing is a fundamental concept in 5G technology. It involves creating multiple virtual networks on a shared physical infrastructure. Each slice is an isolated end-to-end network tailored to meet the specific needs and performance requirements of different applications or services.
Benefits of Network Slicing -
Each slice operates as an independent logical network, ensuring dedicated resources for different services.
Slices can be customized to match the unique requirements of various use cases, such as low latency for autonomous vehicles, high bandwidth for HD video streaming, or enhanced reliability for critical communications.
Purpose of the Project –
The primary goal of this project is to develop a simulation that models a network of base stations and clients. This simulation allows us to test and analyse various 5G scenarios.

## Slide 5: INTRODUCTION
Definition: Network slicing is the practice of creating multiple virtual networks on top of a shared physical network infrastructure. Each virtual network, or "slice," operates as an independent end-to-end network.
Purpose: It allows operators to efficiently allocate resources and provide tailored services for different use cases, such as IoT, enhanced mobile broadband, and ultra-reliable low latency communications (URLLC).
Use – Cases -
IoT: Dedicated slices for IoT devices, ensuring low power consumption and wide area coverage.
Enhanced Mobile Broadband (eMBB): High bandwidth slices for applications like streaming and virtual reality.
URLLC: Slices with ultra-low latency for critical applications like autonomous driving and remote surgery.
MMTC – Massive Machine Type Communication

## Slide 6: INTRODUCTION
What is Network Slicing?
Network slicing is a fundamental concept in 5G technology. It involves creating multiple virtual networks on a shared physical infrastructure. Each slice is an isolated end-to-end network tailored to meet the specific needs and performance requirements of different applications or services.
Benefits of Network Slicing -
Each slice operates as an independent logical network, ensuring dedicated resources for different services.
Slices can be customized to match the unique requirements of various use cases, such as low latency for autonomous vehicles, high bandwidth for HD video streaming, or enhanced reliability for critical communications.
Purpose of the Project –
The primary goal of this project is to develop a simulation that models a network of base stations and clients. This simulation allows us to test and analyse various 5G scenarios.

## Slide 7: APPROACH & METHODOLOGY
This project uses discrete event simulation with Python, Simpy, Matplotlib and KDTree along with asynchronous programming to model and analyse the 5G Network behaviour. The simulation allows for detailed configuration of clients, base stations, slices, and mobility patterns, providing a flexible and powerful tool for exploring various 5G scenarios.
Discrete Event Simulation - Discrete event simulation (DES) is a modelling technique used to represent the operation of a system as a chronological sequence of events. In this case, DES is employed to simulate the interaction between clients and base stations, capturing the dynamic behavior of a 5G network.
Simpy - Simpy is a process-based discrete-event simulation framework for Python. It allows for the easy modelling of concurrent processes in a network simulation.
Matplotlib - Matplotlib is used for plotting and visualizing simulation results, helping in the analysis and presentation of data.
KDTree - KDTree is utilized for efficient spatial searches, crucial for finding the closest base stations to clients in the simulation.
Asynchronous Programming - Asynchronous programming is leveraged to handle multiple tasks concurrently, improving the efficiency and performance of the simulation.

## Slide 8: APPROACH & METHODOLOGY
Configurations –
Clients – Clients in the simulation represent the devices using the network. They generate requests based on predefined parameters, such as usage frequency and distribution patterns.
Base Stations – Base stations provide the necessary resources for the network. They are configured with specific attributes like bandwidth capacity and coverage area
Slices – Slices define different network services within the simulation. Each slice has unique characteristics such as delay tolerance, quality of service (QoS) class, and bandwidth requirements.
Mobility Patterns - Mobility patterns model the movement of clients within the network. Different statistical distributions (e.g., normal, uniform) can be used to represent how clients move around the coverage area.

## Slide 9: INPUT

## Slide 10: OUTPUT

## Slide 11: OUTPUT EXPLANATION
Base Stations (BS):
Definition: A base station is a central communication point for wireless devices (clients) within a specific area.
Function: It transmits and receives signals, providing connectivity and communication services to clients.
Parameters:
Location (x, y): Coordinates indicating the position of the base station.
Coverage: The radius around the base station where it can provide service.
Capacity Bandwidth: The total amount of data that can be transmitted or received per second.
Ratios: The proportion of resources allocated to different types of services (slices).

## Slide 12: OUTPUT EXPLANATION
Average bandwidth usage: Average bandwidth used by all clients during the simulation.
Average load factor of slices: Average ratio of bandwidth used by each slice relative to their capacity.
Average coverage ratio: Average ratio of the area covered by base stations relative to the total simulation area.
Average block ratio: Average ratio of clients that were blocked or unable to connect due to insufficient resources.
Average handover ratio: Average ratio of handovers during the simulation.

## Slide 13: OUTPUT EXPLANATION
Connected Clients Ratio:
This plot shows the ratio of clients that are successfully connected to a base station over time.
The y-axis represents the ratio, and the x-axis represents time steps in the simulation.
A high and stable ratio indicates good connectivity performance.
Coverage Ratio:
This plot displays the ratio of the area covered by base stations relative to the total simulation area.
The y-axis represents the coverage ratio, and the x-axis represents time steps.
A high and stable ratio indicates efficient coverage of the area.
Total Bandwidth Usage:
This plot shows the total bandwidth used by all clients over time.
The y-axis represents bandwidth usage in Gbps, and the x-axis represents time steps.
This helps to understand the network load and bandwidth demand.

## Slide 14: OUTPUT EXPLANATION
Block Ratio:
This plot shows the ratio of clients that were blocked or unable to connect due to insufficient resources.
The y-axis represents the block ratio, and the x-axis represents time steps.
A lower block ratio indicates better performance and resource allocation.
Bandwidth Usage Ratio in Slices (Averaged):
This plot shows the average ratio of bandwidth used by each slice (service type) over time.
The y-axis represents the bandwidth usage ratio, and the x-axis represents time steps.
This helps in understanding the distribution of bandwidth among different service types.
Handover Ratio:
This plot shows the ratio of handovers, where a client switches from one base station to another, over time.
The y-axis represents the handover ratio, and the x-axis represents time steps.
A high handover ratio might indicate high client mobility or poor initial connections.
Client Count Ratio per Slice:
This plot shows the ratio of clients for each slice (service type) over time.
The y-axis represents the client count ratio, and the x-axis represents time steps.
This provides insight into the distribution of clients across different service requirements.
Bottom Right Section: Summary Statistics
This table summarizes key performance metrics from the simulation:

## Slide 15: LITERATURE SURVEY
1) Optimal Slice Allocation in 5G Core Networks
Authors: Danish Sattar, Ashraf Matrawy
Source: IEEE
Summary:
  This paper addresses the challenge of optimally allocating network slices in the 5G core network to enhance efficiency and performance. It proposes a mathematical model for slice allocation that balances resource utilization and service quality.
Key Contributions:
  Optimization Model: Introduces a model that formulates the slice allocation problem as an optimization problem, aiming to maximize resource utilization while meeting the service requirements of each slice.
  Evaluation Metrics: Utilizes metrics such as slice acceptance ratio, resource utilization rate, and service level agreement (SLA) compliance to evaluate the effectiveness of the proposed model.
Relevance to the Project:
  The optimization techniques and evaluation metrics can be incorporated into the project to enhance its capability in simulating and analysing optimal slice allocation strategies.

## Slide 16: LITERATURE SURVEY
2) Slice Admission and Deployment Strategies in Resource-Constrained 5G Network Slices using an Actor-Critic Approach
Authors: Ralph Voltaire J. Dayot, In-Ho Ra
Source: 2022 Joint 12th International Conference on Soft Computing and Intelligent Systems and 23rd International Symposium on Advanced Intelligent Systems (SCIS&ISIS)
Summary:
  This paper explores slice admission and deployment strategies in 5G networks using a reinforcement learning approach, specifically an actor-critic method, to manage resource constraints effectively.
Key Contributions:
  Reinforcement Learning Approach: Applies an actor-critic reinforcement learning framework to dynamically manage the admission and deployment of network slices under resource constraints.
  Performance Evaluation: Demonstrates the effectiveness of the proposed approach through simulations, showing improvements in resource utilization and service quality.
Relevance to the Project :
  The reinforcement learning methodology and performance evaluation techniques can be integrated into the project to simulate advanced slice admission and deployment strategies.

## Slide 17: LITERATURE SURVEY
3) Network Slice Access Selection Scheme in 5G
Authors: Huan Wei, Zhenfeng Zhang, Bin Fan
Source: 2017 IEEE 2nd Information Technology, Networking, Electronic and Automation Control Conference (ITNEC)
Summary:
  This paper presents a network slice access selection scheme for 5G networks, focusing on optimizing the selection process to enhance network performance and user experience.
Key Contributions:
  Access Selection Algorithm: Proposes an algorithm for selecting the optimal network slice for user access, considering factors such as network conditions, user requirements, and slice capabilities.
  Simulation Results: Provides simulation results that demonstrate the algorithm's effectiveness in improving network performance and user satisfaction.
Relevance to the Project :
  The access selection algorithm and its simulation results can inform the development of similar features in the project , allowing for the analysis of access selection strategies.

## Slide 18: LITERATURE SURVEY
4) Performance Enhancement in 5G Cellular Networks Using Priorities in Network Slicing
Authors: Mohammad Shurman, Eyad Taqieddin, Omar Oudat, Raffi Al-Qurran, Abd Alrahman Al Nounou
Source: 2019 IEEE Jordan International Joint Conference on Electrical Engineering and Information Technology (JEEIT)
Summary:
  This paper investigates the use of priority-based mechanisms in network slicing to enhance the performance of 5G cellular networks.
Key Contributions:
  Priority-Based Mechanisms: Proposes a framework that assigns different priority levels to network slices based on their service requirements and criticality.
  Performance Analysis: Analyzes the impact of priority-based slicing on network performance, showing improvements in resource allocation efficiency and service quality.
Relevance to the Project:
  The priority-based mechanisms and performance analysis can be utilized in the project to model and study the impact of prioritization on network performance.

## Slide 19: LITERATURE SURVEY
5) End-to-End 5G Network Slice Resource Management and Orchestration Architecture
Authors: Hiroki Baba, Shiku Hirai, Takayuki Nakamura, Sho Kanemaru, Kensuke Takahashi, Taisuke Omoto, Shinsaku Akiyama, Senri Hirabaru
Source: 2022 IEEE 8th International Conference on Network Softwarization (NetSoft)
Summary:
  This paper presents an end-to-end resource management and orchestration architecture for 5G network slicing, aiming to enhance automation and efficiency in managing network resources.
Key Contributions:
  Orchestration Architecture: Describes a comprehensive architecture that integrates resource management and orchestration functions to support end-to-end network slicing.
  Implementation and Results: Provides implementation details and experimental results that demonstrate the architecture's ability to improve resource management efficiency and service delivery.
Relevance to the Project:
  The proposed architecture and its implementation insights can be integrated into the project to simulate end-to-end resource management and orchestration scenarios.

## Slide 20
THANK - YOU